## Slide 1: WB Carbon Monitor Cities
Residential
Work flow and exploratory analysis
CZ, 2022-07-27

## Slide 2
Total near-real-time
CO2 Emission
Near-real-time Grid CO2 Emission
Near-real-time Grid CO2 Emission = f(Total Emission, Spatial Modifier, Temporal Modifier)
Total regional emission from carbon monitor database
Spatial Modifier
The base emission for the grid
Temporal Modifier
The emission varied with time for the grid
f(building, household, population, land use type, heating/cooking source, …)
f(electricity, nightlight, surface temperature, air temperature, …)
100*100 m

## Slide 3
Near-real-time Grid CO2 Emission in City’s Residential Area
Spatial Modifier
f(Total Emission,
Spatial Modifier,
Temporal Modifier)
Buildings
Spatial res:
100*100 m or 500*500 m
Temporal res:
Daily or weekly
Temporal Modifier
Electricity,
VIIRS nightlights, …
Energy consumption
Climate
Air temperature,
Land surface temperature, …
Economic indicator
Land use/cover
Population, Households
GDP, energy source,
Cooking/heating source, …
LCZ, human settlement layer, google landcover, …
Microsoft database (unlabeled)
Area, Height, Type
ML model based on Open street map Buildings (OSMB) and other land use/cover datasets
Building Prediction
Output
Emission estimator
Total near-real-time CO2 emission
(from carbon monitor database)

## Slide 4
Level | data | source
Country level | heating/cooking source | Census data or governmental statistical data
 | energy structure | 
 | GDP | 
 | Poverty | 
 | Other economic indicator | 
City/division level | Population | 
 | household number | 
 | household size | 
Polygon level | Building number | ML model output trained with MS building dataset, OSMB dataset, and other grid-based dataset, such as LCZ, Copernicus DEM, night light, …
 | Building area, type, level | 
Grid level | LCZ (100*100m) | https://zenodo.org/record/6364594#.YsgpS3ZBybg
 | Human settlement layer | https://ghsl.jrc.ec.europa.eu
 | VIIRS nightlights | https://eogdata.mines.edu/products/vnl/
 | Google land cover | https://blog.google/products/earth/dynamic-world-land-cover-data/
 | Copernicus DEM | https://spacedata.copernicus.eu/web/cscda/dataset-details?articleId=394198
 | Land surface temperature | 
 | Air temperature | ERA5 model
Datasets
Note: the datasets are not limited in those are listed, and we will replace some of those datasets if we find some alternative dataset with higher quality.

## Slide 5: Region defines
Regions need to be defined with boxes
  Administrative divisions include large non-urban areas (not of our interests)
  Continuous urban areas are divide into parts by administrative division
Uncertainties
  We assume the selected regions has the same administrative region data, such as population, household number, …

## Slide 6: How we select the region
The most populated region (urban area) for the proposed cities will be included.
The closely adjacent populated regions will also be included until the we see a clear break of the urban area, or the region become too large.
We adjust the region based on the MS buildings and LCZ maps (world urban database, https://www.wudapt.org/lcz-maps/)
  Most of the dense building areas (both MS buildings and LCZ categories) are included in our regions

## Slide 7: LCZ class and color scheme
Dense over 10 stories
Dense 3-9 stories
Dense 1-3 stories
Over 10 stories
3-9 stories
1-3 stories
Dense 1 story
Large 1-3 stories
Industrial
Buildings in nature land cover
Dense trees
Scatter trees
Bush
Rock
Low plants
Water
Sand

## Slide 8
Cairo
Top left: (30.4, 30.8),
Bottom right:(29.7, 31.8)
Microsoft building
Johannesburg
Top left:(-25.7, 27.7),
Bottom right:( -26.6, 28.5)

## Slide 9
Adana
Top left:(37.1, 35.2),
Bottom right:(36.9, 35.5)
Ordu
Top left:(41.02, 37.85),
Bottom right:( 40.92, 38.03)

## Slide 10
Trabzon
Top left:(41.02, 39.65),
Bottom right:( 40.95, 39.80)
Manisa
Top left:(38.67, 27.28),
Bottom right:(38.58, 27.49)

## Slide 11: V1: gridded map with no time variance
Add polygon layers, such as administrative division, buildings, …
Add raster layers, such as LCZ, night light, …
Bind data to polygons layers, such as population, area, …
Rasterize the polygon layers (polygon -> raster)
Unify the resolution for all the raster layers
Calculate emission raster
Make output dataset and visualization
Polygon layers
Polygon + raster layers
Rasterize
Building area
Building density

## Slide 12
Simple emission = (density + area*lcz_height)* population
Higher resolution is also possible
Base resolution
500*500 m
Example output for Ordu

## Slide 13: Timeline
clean and re-organize code and data: 2 weeks, Oct. 6th
  Clean the code structure
  Make the pipeline possible to plug any dataset
  Add a module that predict building features
Emission map based on large-small grid: 2 weeks, Oct 20th
  The emission will be firstly disaggregated with coarse but important layers, such as nightlight
  The emission will be further disaggregated with fine layers inside the coarse layer grid
  E_builidng = E_tot * (W_coarse * M_coarse) * (W_fine * M_fine) * M_building
    E: emission
    W: weight based on layer
    M: modifier based on grid/building property
Final outputs: 1 week, Oct. 28th